## Slide 1: THU SUMMER SCHOOL 2025
CHANTAL DEUSCH | JEREMY DIEM | JAN GASCHLER | SERHAT GÜREL | PAULINA PYCZOT | VALENTIN TALMON-L‘ARMÉE
Image Detection with YOLO AI on a Raspberry Pi

## Slide 2: Agenda
Setup Raspberry Pi
Licence Plate Recognition
Face Recognition

## Slide 3: Visual Process Structure
Raspberry Pi
Taking Pictures
Detect Plate
Reading Plate
Live Stream
Detect Person and Face
Learn Face

## Slide 4: Set Up Raspberry Pi
To set up the Raspberry Pi, you will need the following physical components:
SDHC card
USB-compatible camera
SDHC Adapter
External PC/Laptop
Ethernet Switch/Internet connection

## Slide 5: Preparing the SDHC Card
Formatting the SDHC Card and installing Raspberry Pi OS
First, you need to download and install the Raspberry Pi Imager Software on your Computer: https://www.raspberrypi.com/software/
Once installed, you’ll be greeted with the options to choose a model, an OS and an SDHC Card
For the model, we’ll choose Raspberry Pi 4 and for the Operating System (OS) Raspberry Pi OS (64-bit)

## Slide 6: Preparing the SDHC Card
Formatting the SDHC Card and installing Raspberry Pi OS
Then you need to select the inserted SDHC Card where the OS should be installed by clicking “Choose SD Card”
Finally, you need to click on continue and then “Edit settings” and then “Services” and then tick the “Enable SSH” option to enable the ssh server for the connection later
After this, hit save, yes and yes

## Slide 7: Enable vnc using ssh
Use the IP Adress of the Raspberry Pi to ssh onto the Pi using ssh pi@[IP] Password: raspberry
Then use sudo raspi-config to enter the Raspberry Pi Configuration menu
In the menu navigate to Interface Options and enter
In the Interface options navigate to VNC and enter
In the popup select Yes and enter
Now the VNC server is ready to use, you can exit the configuration menu now
You can connect using your favorite VNC Viewer using [IP of the Pi]:5900 and the already known user credentials

## Slide 8: Preparing the venv environment
Creating and using a venv environment
Using the Raspberry Pi Terminal you can create and use a Python Virtual Environment
First, type python3 -m venv environment in the terminal
Then enable the created venv environment using source environment/bin/activate
Now we can go over to prepare the libraries using our Script

## Slide 9: Preparing the needed libraries
First, you need to clone the GitHub Repositery using: git clone https://github.com/TOPR-yoloteam/YOLO-Hands-On-Tutorial.git
Then you need to go into the utils folder using: cd YOLO-Hands-On-Tutorial/src/hands_on_tutorial/utils
Now execute the bash file using: bash libraries.bash
Now all the needed libraries and everything else will be automatically installed and ready to use!

## Slide 10: Setup Raspberry Pi
Thonny
A simple and beginner-friendly Python development environment
Pre-installed on Raspberry Pi OS
Built-in debugger
How to Start and Use Thonny
Type thonny in the Terminal
Use the file explorer to navigate to the Python file you want to edit by using the Load button
To run the script, click the green Run button at the top (or press F5 on your Keyboard)
Setting Up the Python Development Environment

## Slide 11: License Plate Recognition

## Slide 12: License Plate Recognition
To see changes better, use the following code after changing an image
Code to be written is marked with #TODO X in the source code
Google loves you, ChatGPT doesn't <3
Helpful tips

## Slide 13: License Plate Recognition
To recognize license plates, we need images. These images must be captured first. We do this using the Image class in the make_images.py file.
  Run the script to start capturing images from the webcam
Taking Pictures​

## Slide 14: License Plate Recognition
Taking Pictures​ / Solution
Um Bilder zu erstellen, das Skript make_images.py entweder über Thonny oder (empfohlen) CLI ausführen
  Mit cd in den jeweiligen Ordner navigieren
  python make_images.py

## Slide 15: License Plate Recognition
In order to be able to read the text from license plates later, we must first recognize the license plate as such
Task 1: Modify the Python code to detect a license plate and draw its corresponding bounding box
Hint: The Ultralytics docs homepage provides information on how to use a YOLO model :')
Detect License Plate

## Slide 16: License Plate Recognition
Detect License Plate / Solution
To get the Class ID students have to analyze the NCNN model (directory)
Model -> license_plate_detector_ncnn_model -> metadata.yml
read class_id

## Slide 17: License Plate Recognition
To achieve the best OCR results, we now want to save the license plate as a single image
Task 2: Save the license plate as a single image in a seperate folder named "license_plates"
Hint: Use the plates bounding box coordinates!
Detect License Plate

## Slide 18: License Plate Recognition
Detect License Plate / Solution

## Slide 19: License Plate Recognition
Colored images can cause problems in character recognition, therefore we need to preprocess the input image
Task 1: Preprocess Image on color, threshold, dilation and contours
Hint: Use the OpenCV library for image preprocessing. For contours use the given method "find_and_sort_contours"
Read License Plate

## Slide 20: License Plate Recognition
Read License Plate / Solution

## Slide 21: License Plate Recognition
Read License Plate / Solution

## Slide 22: License Plate Recognition
Read License Plate / Solution

## Slide 23: License Plate Recognition
If all steps are done correctly, start with the OCR!
Task 2: Extract text from the contours and print the results
Hint: What does "extract_text_from_contours" return?
Read License Plate

## Slide 24: License Plate Recognition
Read License Plate / Solution

## Slide 25: Face Recognition

## Slide 26: Face Recognition
In this tutorial, we explore how the YOLOv8n-face model can be used to detect human faces in real time
The YOLOv8n-face architecture is fine-tuned specifically for faces, combining high detection accuracy with a relatively small model size (only 1 object class)
Although YOLO is highly optimized for GPU acceleration and real-time performance, it tends to lag more than MediaPipe, especially on resource-constrained devices like a Raspberry Pi
A framework by Google providing lightweight models, particularly FaceMesh for detailed facial landmark detection.
Often highly performant, even on resource-constrained devices like the Raspberry Pi.
Focuses on extracting facial features (landmarks) which can then be used for recognition by comparing their relative positions.
YOLO
MediaPipe
Please choose between:

## Slide 27: Face Recognition
Task 1:
Implement face detection based on YOLO.
Detect faces and draw bounding boxes around them.
YOLO
If you want to solve the MediaPipe exercises, please skip to page 33

## Slide 28: Face Recognition
Task 1.1:
Ensure the self.model_path correctly points to the "yolov8n-face.pt" file within the project structure.
Task 1.2:
You run detection by calling the model object directly: results = self.model(...).
Pass the video frame as the main argument to the model.
Crucial: Use the classes=[0] argument to tell the model to only detect faces (which is class 0 in this specific face model).
Task 1.3:
The results object contains detections. You often need to loop through results, then result.boxes, then each box.
The coordinates are typically stored within a box object, often under the attribute .xyxy[0].
The coordinates might be floating-point numbers. Use map(int, ...) to convert them to integers before drawing.
  Example: x1, y1, x2, y2 = map(int, box.xyxy[0])
YOLO Task 1 tips

## Slide 29: Face Recognition
Task 1.4:
You can use OpenCV's drawing function: cv2.rectangle(...).
Remember the required arguments: cv2.rectangle(image, pt1, pt2, color, thickness).
  pt1 is the top-left corner (x1, y1).
  pt2 is the bottom-right corner (x2, y2).
  Color is a BGR tuple, e.g., (0, 255, 0) for green.
  Thickness is an integer, e.g., 2.
YOLO Task 1 tips

## Slide 30: Face Recognition
Task 2:
Extend the system by adding face recognition. Person detection is already provided. Implement recognizing known faces and mark them in the image.
YOLO
If you want to solve the MediaPipe exercises, please skip to page 33

## Slide 31: Face Recognition
Task 2.1:
Make sure you're reading image files from the correct directory (self.faces_dir).
Use face_recognition.load_image_file() to load each image.
Get the face encoding using face_recognition.face_encodings(loaded_image)[0].
  Note the [0] assumes one face per known image file.
Store the encoding in self.known_face_encodings and the name (from filename) in self.known_face_names. Keep these lists synchronized!
Task 2.2:
Get the face_location passed to the save_face function.
Crop the face from the stored self.current_frame using these coordinates: face_image = self.current_frame[top:bottom, left:right].
Consider expanding the coordinates slightly before cropping to get more context, but be careful not to go outside the frame boundaries (max(0, ...), min(width, ...)).
Save the face_image using cv2.imwrite() into self.faces_dir. Give it a filename based on the entered name.
Very Important: After saving, immediately call self.load_known_faces() again so the system recognizes the newly added person right away.
YOLO Task 2 tips

## Slide 32: Face Recognition
Task 2.3, 2.5., 2.6, 2.7:
Use the self.state variable ("normal" or "entering_name") to control behavior.
In mouse_callback: If state is "normal", check if the click (x, y) is inside any stored button area. If yes, change self.state to "entering_name" and store which face was clicked (self.selected_face_loc).
In the main loop (run): If self.state is "entering_name", handle keyboard input (cv2.waitKey(1)):key == 13 (Enter): Save the face if self.current_text is not empty, then switch back to "normal" state.
  key == 27 (Esc): Switch back to "normal" state.
  key == 8 (Backspace): Remove last character from self.current_text.
  Printable characters: Append chr(key) to self.current_text.
Draw the text input UI (draw_text_input) and highlight the selected face only when in the "entering_name" state.
YOLO Task 2 tips

## Slide 33: Face Recognition
Task 2.4:
You need face locations and encodings for the current video frame first.
Use face_recognition.face_locations() and face_recognition.face_encodings().
Remember: Convert the OpenCV frame (BGR) to RGB before passing it to face_recognition functions: rgb_frame = cv2.cvtColor(frame, cv2.COLOR_BGR2RGB).
Use face_recognition.compare_faces(self.known_face_encodings, encoding_to_check) to get potential matches.
Use face_recognition.face_distance(self.known_face_encodings, encoding_to_check) to find the distance for each comparison. Lower distance means a closer match.
Find the best match using np.argmin(face_distances) on the distances array.
Verify the best match: Check if matches[best_match_index] is True.
YOLO Task 2 tips

## Slide 34: Face Recognition
Task 2.4:
Draw the name label using cv2.putText().
Draw the "Learn Face" button (using cv2.rectangle and cv2.putText) only if the face is "Unknown" and the system is in the "normal" state.
For the button click to work later, store the button's screen coordinates and the corresponding face location (top, right, bottom, left) together (e.g., in self.button_area).
YOLO Task 2 tips

## Slide 35: Face Recognition
Task 1:
Implement face detection based on MediaPipe.
Face recognition is not required in this task.
Detect faces and draw bounding boxes around them.
MediaPipe
If you want to solve the YOLO exercises, please go back to page 25

## Slide 36: Face Recognition
Task 1.1:
Create the FaceMesh instance using mp.solutions.face_mesh.FaceMesh(...).
You can set parameters like max_num_faces=... and min_detection_confidence=... during initialization (check MediaPipe documentation for details).
Task 1.2:
Important: MediaPipe expects images in RGB format, but OpenCV captures in BGR. Convert the frame: image_rgb = cv2.cvtColor(frame, cv2.COLOR_BGR2RGB).
Call the process() method on your self.face_mesh object, passing the image_rgb.
Task 1.3:
Use OpenCV's cv2.rectangle(image, pt1, pt2, color, thickness).pt1 should be the top-left corner: (left, top).pt2 should be the bottom-right corner: (right, bottom).
Choose a color (BGR tuple like (0, 255, 0) for green) and thickness.
MediaPipe Task 1 tips

## Slide 37: Face Recognition
Task 2:
Extend the system by adding face recognition.
Person detection is already provided.
Implement recognizing known faces and mark them in the image.
MediaPipe
If you want to solve the YOLO exercises, please go back to page 25

## Slide 38: Face Recognition
Task 2.1:
You don't need all 400+ landmarks from FaceMesh. Use the provided key_landmarks_indices list to select a smaller, specific set (e.g., 50 landmarks).
Loop through key_landmarks_indices. For each index idx, get the landmark data: landmark = face_landmarks.landmark[idx].
Store the normalized coordinates landmark.x and landmark.y (values between 0.0 and 1.0).
Create a flat NumPy array from these coordinates (e.g., [x1, y1, x2, y2, ..., x50, y50]). The size must be consistent!
Task 2.2:
This happens in the compare_landmarks function.
You need to compare the detected landmarks array to every stored landmark sample for every known person (for known_landmarks in person_landmarks_list:).
A good way to measure similarity is the Euclidean distance: distance = np.linalg.norm(landmarks - known_landmarks).
Keep track of the min_distance found and the best_match_index (which person it corresponds to).
MediaPipe Task 2 tips

## Slide 39: Face Recognition
Task 2.3:
After checking all known landmarks, take the overall min_distance.
Compare it to self.recognition_threshold.
If min_distance < self.recognition_threshold, it's a match! Set is_known_face = True and get the name using best_match_index.
If the distance is larger, it's "Unknown" (is_known_face = False).
Consider calculating a confidence score based on how far below the threshold the distance is.
MediaPipe Task 2 tips

## Slide 40
QUESTIONS TIME!
Have a question? Ask NOW!

## Slide 41: AB HIER IST DIE PPT FÜR DEN PROF

## Slide 42: Folie mit einzeiligem Text
Text als Aufzählung
  Mit mehreren Ebenen möglich
Oder einfach als Fließtext
Lorem ipsum dolor sit amet, consetetur sadipscing elitr, sed diam nonumy eirmod tempor invidunt ut labore et dolore magna aliquyam erat, sed diam voluptua. At vero eos et accusam et justo duo dolores et ea rebum.
Lorem ipsum dolor sit amet, consetetur sadipscing elitr, sed diam nonumy eirmod tempor invidunt ut labore et dolore magna aliquyam erat, sed diam voluptua.
Mit optionaler Subline

## Slide 43: Abschnittstitel mit Bild
Hier steht die Subline

## Slide 44: Abschnittstitel ohne Bild
Hier steht eine Subline

## Slide 45: Abschnittstitel auf Blau (nur digitale Anwendungen)
Hier steht die Subline

## Slide 46: Folie mit zwei Text-Spalten
Lorem ipsum dolor sit amet
Consetetur sadipscing elitr
Sed diam nonumy eirmod
Tempor invidunt ut labore et dolore magna aliquyam erat
Sed diam voluptua.
Lorem ipsum dolor sit amet
Consetetur sadipscing elitr
Sed diam nonumy eirmod
Tempor invidunt ut labore et dolore magna aliquyam erat
Sed diam voluptua.
Mit optionaler Subline

## Slide 47: Folie mit drei Text-Spalten
Lorem ipsum dolor sit amet
Consetetur sadipscing elitr
Sed diam nonumy eirmod
Tempor invidunt ut labore et dolore magna aliquyam erat
Sed diam voluptua.
Lorem ipsum dolor sit amet
Consetetur sadipscing elitr
Sed diam nonumy eirmod
Tempor invidunt ut labore et dolore magna aliquyam erat
Sed diam voluptua.
Mit optionaler Subline
Lorem ipsum dolor sit amet
Consetetur sadipscing elitr
Sed diam nonumy eirmod
Tempor invidunt ut labore et dolore magna aliquyam erat
Sed diam voluptua.

## Slide 48: Folie mit Text- und Bild-Spalte
Lorem ipsum dolor sit amet
Consetetur sadipscing elitr
Sed diam nonumy eirmod
Tempor invidunt ut labore et dolore magna aliquyam erat
Sed diam voluptua.
Mit optionaler Subline

## Slide 49
Text auf Bild mit transparentem Hintergrund

## Slide 50: Folie mit Tabelle
Spalte 1 | Spalte 2 | Spalte 3
Zelle 1 | Zelle 2 | Zelle 3
Tabellen in verschiedenen Farbvarianten möglich
Spalte 1 | Spalte 2 | Spalte 3
Zelle 1 | Zelle 2 | Zelle 3
Spalte 1 | Spalte 2 | Spalte 3
Zelle 1 | Zelle 2 | Zelle 3

## Slide 51: Folie mit Diagrammen
Chart: 
| Kategorie 1 | Kategorie 2 | Kategorie 3 | Kategorie 4
Datenreihe 1 | 4.3 | 2.5 | 3.5 | 4.5
Datenreihe 2 | 2.4 | 4.4 | 1.8 | 2.8
Datenreihe 3 | 2 | 2 | 3 | 5
Ansicht verschiedener Diagramm-Typen
Chart: Diagrammtitel
| 1. Quartal | 2. Quartal | 3. Quartal | 4. Quartal
Verkauf | 8.2 | 3.2 | 1.4 | 1.2
Chart: 
| Kategorie 1 | Kategorie 2 | Kategorie 3 | Kategorie 4
Datenreihe 1 | 4.3 | 2.5 | 3.5 | 4.5
Datenreihe 2 | 2.4 | 4.4 | 1.8 | 2.8
Datenreihe 3 | 2 | 2 | 3 | 5

## Slide 52: THU-Farben
Übersicht der vorgegebenen Farben

## Slide 53: Vielen Dank für Ihre Aufmerksamkeit.
www.thu.de

## Slide 54: Folie mit Smart-Art Grafiken
Profil-felder
Marken-kern
Marken-nutzen
Werte
Ansicht verschiedener Grafik-Layouts
Prozess 1
Prozess 2
Prozess 3
Konsistenz
Konsequenz
Kompetenz

## Slide 55: Prozess / Folge / Zusammenhang
Titel 1
Titel 3
Titel 2
Titel 4
XXX
XXX
XXX
XXX

## Slide 56: Themen / SWOT Analyse / Zusammenhang
Titel 1
Titel 2
Titel 4
Titel 3
Sed ut perspiciatis unde omnis iste natus error sit ametr sit voluptatem laudantium, totam ak rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi voluptatem sequi nesciunt.
Sed ut perspiciatis unde omnis iste natus error sit ametr sit voluptatem laudantium, totam ak rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi voluptatem sequi nesciunt.
Sed ut perspiciatis unde omnis iste natus error sit ametr sit voluptatem laudantium, totam ak rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi voluptatem sequi nesciunt.
Sed ut perspiciatis unde omnis iste natus error sit ametr sit voluptatem laudantium, totam ak rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi voluptatem sequi nesciunt.

## Slide 57: Themenverbindung
Zusammenfügen unterschiedlicher Kompetenzen / Themen
At vero eos et accusamus et iusto odio ducimus blanditiis praesentium.
At vero eos et accusamus et iusto odio ducimus blanditiis praesentium.
At vero eos et accusamus et iusto odio ducimus blanditiis praesentium.
Thema 3
Thema 2
Thema 4
At vero eos et accusamus et iusto odio ducimus blanditiis praesentium.
Thema 1

## Slide 58: Step By Step
01
02
03
04
05
Olizevero eos et accusamus et ius odio ducimus.
Olizevero eos et accusamus et ius odio ducimus.
Olizevero eos et accusamus et ius odio ducimus.
Olizevero eos et accusamus et ius odio ducimus.
Olizevero eos et accusamus et ius odio ducimus.

## Slide 59: Prozentuale Verteilung
Germany
At vero eos et accusamus et iusto odio dignissimos ducimus qui blanditiis praesentium voluptatum deleniti atque corrupti quos.
Spain
At vero eos et accusamus et iusto odio dignissimos ducimus qui blanditiis praesentium voluptatum deleniti atque corrupti quos.
France
At vero eos et accusamus et iusto odio dignissimos ducimus qui blanditiis praesentium voluptatum deleniti atque corrupti quos.
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 17.2 | 3.2
87%
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 4 | 3.2
55%
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
73%

## Slide 60: Themen-Darstellung
Sed ut perspiciatis unde omnis iste natus error sit voluptatem accusantium doloremque laudantium, totam rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi voluptatem sequi nesciunt. Neque porro quisquam est.
Hunde omnis iste natus error sit voluptatem accusantium doloremque laudantium, totam rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi voluptatem sequi nesciunt. Neque porro quisquam est.
Romnis iste natus error sit voluptatem accusantium doloremque laudantium, totam rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi voluptatem sequi nesciunt. Neque porro quisquam est.

## Slide 61: Ablauf-Plan
Ablauf
Begin
First Step
Proceed
Option
Check
End
Beatae vitae dicta sunt explicabo
Beatae vitae dicta sunt explicabo
Beatae vitae dicta sunt explicabo
Beatae vitae dicta sunt explicabo
Beatae vitae dicta sunt explicabo
Beatae vitae dicta sunt explicabo
Entwicklung

## Slide 62
QUESTIONS TIME!
Have a question? Ask NOW!

## Slide 63: Charts / Vergleiche
Vergleiche von Zahlenreihen
Chart: 2016
| Year 2014
Lon | 0.6
Mad | 0.76
Mue | 0.9
Rom | 0.62
London
Madrid
Rom
München
Chart: 2017
| Year 2014
Lon | 0.6
Mad | 0.76
Mue | 0.9
Rom | 0.62
Chart: 2018
| Year 2014
Lon | 0.6
Mad | 0.76
Mue | 0.9
Rom | 0.62
Chart: 2019
| Year 2014
Lon | 0.6
Mad | 0.76
Mue | 0.9
Rom | 0.62

## Slide 64: Grafik inkl. Prozentuale Erfüllung
Chart: 2017
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Series 1 | 4.3 | 1 | 3.5 | 2.4 | 4.1 | 1.5 | 2.6 | 2 | 4.6 | 4.9 | 2.6 | 3.1
Series 12 | 2 | 2.2 | 1 | 3.1 | 4 | 3 | 4
Series 13 | 3 | 1 | 3.5 | 2 | 3 | 1 | 5
50%
75%
25%
At vero eos et accusamus et iusto odio dignissimos ducimus qui blanditiis praesentium voluptatum deleniti atque corrupti quos dolores et quas molestias excepturi sint occaecat. Cupiditate non provident, similique sunt in culpa qui officia deserunt mollitia

## Slide 65: Verlauf / Entwicklung
zzz
yyy
xxx
aaa
bbb
ccc
Text
labore et dolore magnam aliquam quaerat voluptatem. Ut enim ad minima veniam, quis nostrum amok e exercitationem ullam corporis suscipit laboriosam, nisi ut aliquid ex ea commodi consequatur?
Text
Text

## Slide 66: Internet Results You Have
Premium Services
High Definition
Et am harum quidem rerum on facilis est et expedita e distinctio. Nam libero tempore, cum soluta nobis est eligendi dikame optio cumque nihil.
Et am harum quidem rerum on facilis est et expedita e distinctio. Nam libero tempore, cum soluta nobis est eligendi dikame optio cumque nihil.
Global Solutions
Affiliate Programs
Et am harum quidem rerum on facilis est et expedita e distinctio. Nam libero tempore, cum soluta nobis est eligendi dikame optio cumque nihil.
Et am harum quidem rerum on facilis est et expedita e distinctio. Nam libero tempore, cum soluta nobis est eligendi dikame optio cumque nihil.

## Slide 67: Fully Responsive Balance
At vero eos et accusamus et iusto odio dignissimos ducimus qui blanditiis praesentium voluptatum deleniti atque corrupti quos dolores et quas molestias excepturi sint occaecat. Cupiditate non provident, similique sunt in culpa qui officia deserunt mollitia animi, id est laborum et dolorum fuga. Et harum quidem rerum facilis est et expedita distinctio. Nam libero tempore, cum soluta nobis est eligendi optio cumque nihil impedit quo minus id quod maxime placeat facere possimus, omnis voluptas.
Restore Balance

## Slide 68: Titel
New
Languages
Zoom
Skills
Goes
Live

## Slide 69: Vergleiche oder Kombination
Theorie und Praxis
Et harum quidem rerum facilis est et expedita distinctio. Nam libero tempore, cum soluta nobis est delah eligendi optio cumque nihil abo impedit quo minus amarentoi id quod non recusandae. Itaque eje earum rerum hic tenetur a u sapiente delectus.
Et harum quidem rerum facilis est et expedita distinctio. Nam libero tempore, cum soluta nobis est delah eligendi optio cumque nihil abo impedit quo minus amarentoi id quod non recusandae. Itaque eje earum rerum hic tenetur a u sapiente delectus.

## Slide 70: Zeit / Aufwand
Personal
Medium
Business
Professional
4.3s
3.7s
2.1s
0.9s

## Slide 71: Raster
Alle Publikationen der THU folgen einem vorgegebenen Layoutraster, das die Positionierung der einzelnen Elemente definiert.
Für diese Präsentationsvorlage wurde das Raster mittels Führungslinien hinterlegt. Diese lassen sich im Menü „Ansicht“ ein- und ausblenden.
Die Führungslinien helfen auch bei der Positionierung von Bild- und Textelementen.
Bei allen Folien wird das Logo oben rechts abgebildet
Positionierung der einzelnen Elemente

## Slide 72: Fußzeilen und Signaturen anpassen
Durch das anpassen der Fußzeilen können individuelle Texte, wie Titel, Signaturen oder Verfasser ergänzt werden.
Einfügen: „Kopf- und Fußzeile“
Ergänzen von individuellem Text

## Slide 73: Arbeiten mit der Präsentationsvorlage
Für jede neue Folie innerhalb einer Präsentation sollte das passende Layout (einspaltig, zweispaltig, Bildspalte, …) gewählt werden.
Texte und Bilder sollten direkt in den vorgegebenen Feldern platzieren.

## Slide 74: Ändern der Titel-Grafik
Grafik auswählen
Zeichentool > Format > Fülleffekt > Bild…
Bild aus Datei > gewünschtes Bild einfügen
Bildtools > Format > Zuschneiden > Füllbereich
Foto auf gewünschte Größe/Position im Anschnitt anpassen
2)
4)